## Slide 1
Engineering Materials: A Data-Driven Approach to EV Chassis Selection
Systematic analysis of mechanical, physical, and chemical properties to optimize material selection for electric vehicle chassis applications. This comprehensive study leverages advanced analytics to evaluate 1,552 material specifications across 44 heat treatment variants, applying multi-criteria decision frameworks to identify optimal solutions for structural integrity, weight efficiency, and environmental durability.
Project by: Aravindh G | aravindhkrishnan09@gmail.com
Program: DIYguru Data Science & Engineering Analytics Batch 2025 | May 6th, 2025

## Slide 2
Project Roadmap: Systematic Material Analysis
01
Dataset Architecture
Dual-dataset structure: detailed property profiles (Dataset 1) and simplified suitability markers (Dataset 2)
02
Single-Dataset Engineering
Six foundational tasks exploring mechanical properties, design ratios, and environmental compatibility
03
Cross-Dataset Integration
Six advanced tasks merging datasets for discrepancy auditing, outlier detection, and multi-criteria ranking
04
Material Optimization
Final selection framework balancing strength, ductility, weight, and corrosion resistance for EV chassis

## Slide 3
Understanding the Data: Two Complementary Datasets
Dataset 1: Detailed Properties
1,552 materials with comprehensive specifications
Mechanical: Su, Sy, A5, E, G (strength, elasticity, ductility)
Hardness: Bhn, HV (surface resistance metrics)
Physical: ρ (density), μ (friction coefficient)
Environmental: pH compatibility indicators
Metadata: Standards, heat treatments, descriptions
Dataset 2: Simplified Suitability
1,548 materials with binary classification
Core mechanical properties (Su, Sy, E, G)
Physical properties (μ, ρ)
Critical addition: Use Flag (True/False) indicating engineering suitability
Enables validation and cross-verification
Supports binary classification modeling

## Slide 4
Data Quality Foundation: Initial Exploration Results
1552
Total materials analyzed
Spanning 1,225 unique material types
44
Heat treatment variants
From annealing to tempering at various temperatures
750
Missing heat treatment entries
Filled with 'Unknown' mode value
9
Properties with outliers
Su, Sy, A5, Bhn, G, μ, ρ, pH, HV flagged for review
Key data quality actions: Missing values imputed using mode strategy, outliers capped using IQR method to preserve realistic engineering ranges, and duplicates removed to ensure analytical integrity. All string columns standardized by trimming whitespace.

## Slide 5
Cleaning Impact: Ultimate Tensile Strength (Su)
Mean (MPa)
572.75
559.05
Std Dev
326.83
285.05
Maximum
2220
1252.5
Minimum
69
69
Interpretation
Mean decreased 2.4% — extreme outliers artificially inflated average strength
Std dev reduced 12.8% — more consistent, reliable dataset for engineering decisions
Max capped at 1252.5 MPa — unrealistic 2220 MPa value removed using IQR upper bound
Outlier handling transformed an unreliable dataset into a practical engineering reference, eliminating exotic or erroneous values that could mislead material selection for EV chassis applications.

## Slide 6
Yield Strength & Ductility: Cleaned Statistics
Yield Strength (Sy)
Before: Mean 387 MPa, Max 2048 MPa
After: Mean 364 MPa, Max 867.5 MPa
Maximum value capped 57.6% — removed super-alloy outliers not representative of standard automotive steels
Elongation at Break (A5)
Before: Mean 19.3%, Max 70%
After: Mean 17.5%, Max 37%
Extreme ductility values (likely polymers or errors) removed — realistic metal behavior restored for crash analysis
Data quality note: Source data contained non-integer Sy anomalies (e.g., "280 max", "25 max") requiring type conversion and validation before statistical processing. Cleaning reduced standard deviation across all metrics, improving dataset reliability for multi-criteria optimization.

## Slide 7
Material-Treatment Efficiency: Top Performers
1
Highest Overall Efficiency
Steel SAE 51410 – Tempered at 400°F
Composite efficiency score: 85,530
Combines Su, Sy, E, G for maximum structural performance
2
Best Ductility
DIN X6CrNiTi1810 – Unknown treatment
A5 efficiency: 37.0%
Ideal for energy-absorbing crumple zones requiring high elongation
3
Optimal Hardness
Yellow brass C26800 – Unknown treatment
Bhn/HV efficiency: 223.5
Superior wear resistance for contact surfaces and bushings
When analyzing materials individually by type, Steel SAE 51431 achieved the highest efficiency (57,011), while heat treatment analysis revealed Full-hard processing as most effective (55,892.67). However, combined Material × Treatment analysis provides more actionable insights for application-specific selection.

## Slide 8
Design Ratio Analysis: Three Critical Metrics
Strength-to-Hardness
Su / Bhn
Balances tensile strength against wear resistance — critical for machinability and forming operations
Top: Steel SAE 1141 (5.77)
Strength-Ductility Index
Su × A5
Measures energy absorption capacity — vital for crash structures requiring controlled deformation
Top: Steel SAE 30201 (29,341)
Strength-to-Weight
Su / ρ
Optimizes structural efficiency per unit mass — directly impacts vehicle range and handling
Top: Steel 20ChGNR GOST (0.161)

## Slide 9
Engineering Application Mapping
Chassis & Suspension
Requirement: High machinability + strength
Optimal materials:
Steel SAE 1141
DIN 55Cr3
DIN 37Cr4
Strength-to-Hardness ratio of 5.77 enables efficient forming while maintaining structural integrity
Crumple Zones
Requirement: Maximum energy absorption
Optimal materials:
Steel SAE 30201
Steel SAE 30301
Steel SAE 30202
Strength-Ductility indices above 26,000 ensure controlled deformation before failure
Lightweight Structures
Requirement: Minimize weight without sacrificing strength
Optimal materials:
Steel 20ChGNR GOST
Steel 40ChFA GOST
Steel 30ChGT GOST
Strength-to-Weight ratios above 0.160 directly extend EV range

## Slide 10
Hardness Analysis: Critical Data Limitation
217
Brinell Hardness (Bhn)
All materials show identical value after cleaning
230
Vickers Hardness (HV)
Uniform across entire dataset post-processing
13
HV-Bhn Divergence
Consistent 13-unit difference suggests surface-hardened materials
Analytical constraint: Zero variation in hardness metrics prevents correlation analysis and comparative evaluation. This suggests the dataset contains placeholder values, over-normalized data, or represents a single material class. The 13-unit divergence (HV > Bhn) indicates surface hardening — beneficial for wear-resistant applications like gears and pistons.
Implication: Hardness cannot be used as a differentiating factor in material selection. Design decisions must rely on strength, ductility, and density metrics where variation exists.

## Slide 11
Elasticity Relationships: E, G, and μ
Strong Linear Correlation: E vs G
Elastic Modulus (E) and Shear Modulus (G) exhibit proportional relationship, confirming isotropic material behavior across the dataset.
Theoretical relationship: E = 2G(1 + μ)
Linear distribution validates dataset consistency — materials behave predictably under tension and shear, critical for finite element analysis of chassis loading scenarios.
Weak Correlation: E vs μ
Poisson's ratio (μ) shows minimal variation with Elastic Modulus, suggesting μ is independent of stiffness in this material set.
Design Implications
Isotropic confirmation: Simplifies FEA modeling — uniform stiffness in all directions
Predictable behavior: E/G ratio enables accurate shear load calculations
Poisson independence: Lateral strain behavior decoupled from axial stiffness
Application: Suspension components requiring torsional resistance (drive shafts, control arms) can be optimized using G values, while tensile loads (chassis rails) prioritize E.

## Slide 12
Environmental Compatibility: pH Profile
100% Basic pH Classification
All materials in cleaned dataset exhibit alkaline characteristics (pH > 7), optimizing corrosion resistance in basic environments
Marine Applications
Ideal for seawater exposure where salt and algae shift pH alkaline — suitable for coastal EV operations and ship components
Chemical Processing
Prevents corrosion in alkaline solutions — applicable for battery coolant systems and cleaning solution contact surfaces
Biocompatibility Potential
Body fluids operate at pH ~7.4 (slightly basic) — materials suitable for medical device integration or biometric sensors
Surface treatment recommendation: While inherent basic pH provides corrosion resistance, additional coatings (anodizing, galvanization) can extend durability in extreme alkaline environments or provide multi-environment versatility.

## Slide 13
Cross-Dataset Integration: Merging Strategy
1
Dataset Preparation
D2: Removed 4 duplicate materials (NF variants), handled outliers in Su, Sy, G, μ, ρ, stripped whitespace from all string columns
2
Identifier Creation
Generated 'Material_Alias' by concatenating Std + Material + Heat treatment. Replaced 'Unknown' with blanks for D2 matching compatibility
3
ID Mapping
Created synthetic IDs in D2 by mapping from D1 using Material_Alias as key — ensures unique identification across datasets
4
Inner Join Merge
Final merge on Material_Alias + ID: D1 (1,552) + D2 (1,548) → Merged (1,548 records)
Merge success rate: 99.7% (1,548/1,552) — only 4 materials from D1 lacked D2 equivalents, likely due to duplicate removal. High overlap validates dataset compatibility and enables robust cross-verification analysis.

## Slide 14
Discrepancy Audit: Dataset Consistency Validation
94.4%
Property Agreement Rate
1,461 of 1,548 materials show identical Su, Sy, E, G values across datasets
5.6%
Minor Discrepancies
87 materials exhibit small differences, likely from rounding or unit conversion
Statistical Comparison
Mean, standard deviation, max, and min values show negligible change between D1 and D2 after outlier handling:
Su: Mean difference < 1%
Sy: Mean difference < 1%
E: Values identical (normalized)
G: Values identical (normalized)
Validation Outcome
High data integrity confirmed. Both datasets derived from consistent source with minimal processing variation.
The 94.4% agreement rate validates D2's Use Flag as reliable ground truth for suitability classification modeling.

## Slide 15
Use Flag Patterns: Suitability Criteria Discovery
Su (MPa)
568.6
457.7
-19.5%
Lower strength preferred
Sy (MPa)
370.0
303.5
-18.0%
Lower yield acceptable
A5 (%)
17.14
20.60
+20.2%
Higher ductility required
E (MPa)
160,551
205,422
+28.0%
Higher stiffness valued
G (MPa)
64,021
79,578
+24.3%
Shear resistance critical
Key insight: "Use = True" materials prioritize ductility and elastic resistance over raw tensile strength. This suggests suitability criteria favor materials that can absorb energy and maintain dimensional stability under cyclic loads — ideal for EV chassis subjected to vibration and impact.

## Slide 16
Multi-Criteria Material Ranking Framework
Scoring Methodology
Normalization: Min-max scaling (0-1 range) for Su, A5, ρ; Z-score for outlier-sensitive properties
Weighting scheme:
35% — Ultimate Strength (Su)
25% — Ductility (A5)
15% — Inverse Density (1/ρ)
15% — pH neutrality score
-10% — Poisson's ratio penalty (abs(μ - 0.3))
Formula:Score = 0.35×Su_norm + 0.25×A5_norm + 0.15×(1-ρ_norm) + 0.15×pH_score - 0.10×μ_penalty
Top 5 Materials by Composite Score
Steel SAE 30201 (annealed) — Score: -27.046
Steel SAE 30301 (annealed) — Score: -27.056
Steel 12Ch25N16G7AR GOST 5949-75 — Score: -27.058
Steel SAE 51431 (tempered 400°F) — Score: -27.061
Steel SAE 51416 (tempered 400°F) — Score: -27.061
Note: Negative scores result from penalty term; rankings remain valid (lower = better after normalization).
Application guidance: SAE 30201/30301 excel in ductility-critical zones (crumple structures), while SAE 514xx series offers superior hardness for suspension mounting points requiring wear resistance.

## Slide 17
Outlier Material Detection: Three Failure Modes
High Strength, Low Ductility
Materials exhibiting Su > 1000 MPa but A5 < 5% — brittle behavior under impact loads. Risk: Catastrophic failure without warning deformation in crash scenarios. Example use: Limited to non-structural fasteners or static mounts.
Extreme Resistivity Anomalies
Materials exceeding 95th percentile in electrical resistance — atypical for metallic chassis materials. Implication: Potential grounding issues or electromagnetic shielding problems. Requires verification if aluminum alloys or composites are present.
Hardness Scale Inconsistency
No materials showed HV vs Bhn divergence beyond threshold after cleaning. Result: Dataset exhibits uniform surface treatment characteristics — validates consistent processing but limits hardness-based differentiation.

## Slide 18
Material Descriptor Analysis: Keyword Insights
Hardening: 77 Materials
Average properties:
Su: 812.84 MPa
Sy: 582.62 MPa
A5: 12.39%
ρ: 7860 kg/m³
High strength, moderate ductility — ideal for structural members requiring wear resistance
Corrosion-Resistant: 8 Materials
Average properties:
Su: 775.00 MPa
Sy: 473.81 MPa
A5: 24.00%
ρ: 7873.75 kg/m³
Superior ductility (24% vs 12%) — optimal for exposed body panels and undercarriage
Ductile keyword: Zero matches in dataset — suggests descriptor field lacks standardized terminology. Materials with A5 > 20% exist but aren't explicitly labeled "ductile." Recommendation: Implement semantic search or property-based filtering rather than text matching for material discovery.

## Slide 19
Final Recommendation: EV Chassis Material Selection
Primary Structural Rails
Material: Steel SAE 51410 (Tempered 400°F)
Justification: Highest composite efficiency (85,530), optimal strength-to-weight ratio (0.160), superior hardness for mounting point durability
Properties: Su: 1252 MPa, Sy: 867 MPa, E: 206 GPa
Crumple Zones & Bumper Reinforcements
Material: Steel SAE 30201 (Annealed)
Justification: Maximum strength-ductility index (29,341), A5: 37% enables controlled energy absorption, top multi-criteria score
Properties: Su: 793 MPa, Sy: 304 MPa, elongation optimized for crash performance
Suspension Components
Material: Steel SAE 1141
Justification: Best strength-to-hardness ratio (5.77) ensures machinability + fatigue resistance, Bhn: 217 provides wear resistance for articulating joints
Properties: Balanced Su/Sy for cyclic loading, optimized for forging operations
Corrosion-Exposed Panels
Material: DIN X6CrNiTi1810 or Corrosion-Resistant subset (8 materials)
Justification: A5: 24% (vs 12% hardened steels), alkaline pH compatibility, stainless chemistry for underbody/coastal environments
Properties: Lower strength acceptable for non-structural panels, ductility prevents stress corrosion cracking

## Slide 20
Conclusion: Data-Driven Material Optimization
Dataset Integrity
Rigorous cleaning achieved 94.4% cross-dataset agreement, outlier handling reduced variance 12-28%, enabling reliable analysis
Multi-Criteria Framework
Weighted scoring (35% strength, 25% ductility, 15% weight, 15% pH, -10% μ penalty) identified optimal materials for four chassis zones
Application Mapping
Use Flag analysis revealed ductility + elastic modulus prioritized over raw strength — confirms energy absorption focus for EV safety
Engineering Impact
Recommended material suite balances crashworthiness (SAE 30201), structural efficiency (SAE 51410), machinability (SAE 1141), and corrosion resistance (X6CrNiTi1810) for comprehensive EV chassis performance
Future work: Integrate cost analysis, validate recommendations through finite element crash simulations, expand dataset to include aluminum alloys and composites for further weight reduction opportunities.